## Slide 1: Toxic E-waste Dumped In Developing Countries

## Slide 2: E-waste Defined by US Environmental Protection Agency
Electrical and electronic equipment that is dependent on electric currents or electromagnetic fields in order to function
E-waste may include
  Consumer/entertainment electronics
  Devices of office, information and communications technology
  Household appliances
  Lighting devices
  Power tools
  Devices used for sport and leisure

## Slide 3: Electrical vs Electronic E-waste
Electrical e-waste
  Products that use electricity primarily for energy
    Washing machine
    Power tools
    Refrigerator
Electronic e-waste
  Products that use electricity to manipulate data
    Desktop, Laptop
    Smartphones
    Game consoles
    Televisions

## Slide 4: E-waste Hazardous Materials
Arsenic
Barium
Beryllium
Brominated flame retardants (BFRs)
Cadmium
Chromium
Lead
Mercury
Polychlorinated biphenyls (PCBs)
Polyvinyl chloride (PVC)
Selenium

## Slide 5: Arsenic
Present in
  circuit boards
  LCD displays
  computer chips
Strong link between arsenic exposure and:
  lung cancer
  skin cancer
  bladder cancer

## Slide 6: Barium
Present in
  cathode ray tubes (CRT)
Strong link between barium exposure and
  heart disease
  nervous system disorders
    numbness
    muscle weakness
  stomach and intestine disorders

## Slide 7: Beryllium
Present in
  power supply boxes
Strong link between beryllium exposure and
  Lung cancer
    considered a Group 1 - Carcinogenic
  affects liver, kidneys, heart, nervous system, and the lymphatic system.

## Slide 8: Brominated flame retardants (BFRs)
Present in
  plastic parts
  cable insulation
Link between BFR exposure and
  Thyroid cancer
Notes: Fire retardants for plastics

## Slide 9: Cadmium
Present in
  rechargeable batteries
  CRT screens
  printer ink cartridges and toners
  printer drums
Strong link between cadmium exposure and
  Lung disease
  Kidney failure

## Slide 10: Chromium VI
Present in
  Data tapes
  Floppy discs
Strong link between chromium VI exposure and
  Lung cancer
  Kidney disease
  Liver disease

## Slide 11: Lead
Present in
  CRT screens
  Batteries
  Printed circuit boards
Strong link between lead exposure and
  Decreased intelligence in children
  Nerve disorders
  Fertility problems
  Memory and concentration problems

## Slide 12: Lithium
Present in
  Li-batteries
Hazards of lithium exposure
  Contact with eyes causes caustic irritation or burn
  Reacts with body moisture to cause chemical burns

## Slide 13: Mercury
Present in
  LCD back lights
  Batteries
  Switches
Hazards of mercury exposure
  Damage to nervous system
  Damage to muscles

## Slide 14: Nickel
Present in
  Electron gun in CRT screens
  Batteries
Hazards of nickel exposure
  Lung cancer
  Neurological deficits
  Cardiovascular disease

## Slide 15: Zinc Sulfide
Present in
  CRT screens
Hazards of zinc sulfide
  When burned causes “brass founders” disease
    characterized by malaria like symptoms

## Slide 16: Dioxins
Environmental pollutants
Typically byproducts of industrial processes
Stored in fatty tissue
Half life is 7 to 11 years
  Persistent in the environment
Effects
  nervous system
  immune system
  endocrine system
  proven to cause cancer

## Slide 17: Amount of Hazardous Materials in 30 lb. PC
15 lb. – Plastics
4.3 lb. – Lead
0.693 g – Mercury
0.409 g – Arsenic
2.961 g – Cadmium
1.98 g – Chromium
9.92 g – Barium
4.94 g – Beryllium

## Slide 18: Issues About Consumer Electronic E-waste
E-waste currently makes up between 1 to 2 percent of municipal solid waste
Growing number of consumer electronic products
  438 million consumer products were sold in 2009
  Doubling since 1997
  Smartphone units increased by seven fold between 1997 - 2009
Disposing e-waste in landfills is not an optimal solution
  Manufacturing inputs are high in energy and comprise scarce resources
  Highly toxic materials are included in consumer electronic products

## Slide 19: General Problems with Landfills
Landfills are toxic
  toxic substances in products dumped in landfills leach into soil and groundwater
Landfills form leachate
  water the percolates through waste extracting and becoming toxic
Landfills produce greenhouse gases
  methane is 21 time more potent than carbon dioxide in trapping heat
Landfills not properly designed and managed are dangerous to human health
  Nigeria with 155 million people does not have a licensed landfill

## Slide 20: States Regulate Landfills
Twenty-five states have e-waste laws on the books
Orange states have some regulations regarding disposal of e-waste
NEW JERSEY
Beginning 2011 it is illegal to discard e-waste in general trash.
All businesses and households must recycle electronic items

## Slide 21: Business of E-recycling Emerges
Given new restrictions traditional scrap dealers stepped in
Offered a new service now in demand
  renamed the business “e-recyclers”
For a fee the e-recyclers take e-waste and dispose of it
Recycling e-waste is labor intensive
E-waste however is not profitable to recycle

## Slide 22: Recycling a Cathode Ray Tube (CRT)
CRTs contain toxic substances and are considered hazardous waste
Recyclers can recover a few dollars worth of copper
Recycling a CRT responsibly results in a net loss
Someone has to pay to properly recycle a CRT
Exploiting the available labor in developing countries makes it profitable
  Labor is cheap
  Environment laws unenforced
  Labor safety laws unenforced
It can be ten times more profitable to export e-waste abroad

## Slide 23: Basel Convention
The Basel Convention on the Control of Transboundary Movements of Hazardous Wastes and their Disposal
Negotiated under United Nations Program
Goal is to promote environmentally sound management of exported and imported waste
United States signed but did not ratify
Despite convention e-waste still makes its way from Europe

## Slide 24: Where Does e-waste Go To?
Africa
  Ghana
  Nigeria
China
Vietnam
Malaysia
India
Indonesia
Pakistan

## Slide 25: Primitive Recycling Methods Used in Developing Countries
Use hands to break apart components for
  gold, silver, copper and chips
Cook circuit boards to melt solder
  remove chips
Burn wire to extract copper
  burning creates dioxins
Use acid baths to remove gold from microchips
  dump used acid into river

## Slide 26: Two Infamous e-waste locations
Guiyu, China
Accra, Ghana

## Slide 27: Guiyu, China
Notes: Pronounced Gwhy - you

## Slide 28
Chips removed from circuit boards are soaked in acid to remove small amounts of gold. Acid waste is dumped into fields and rivers
Basel Action Network (BAN)

## Slide 29
Circuit board is cooked over heat to melt solder and then remove electronic components
Basel Action Network (BAN)

## Slide 30
Workers suffer chronic exposure to lead and dioxins emitted from melting solder
Basel Action Network (BAN)

## Slide 31
Fish are caught and cleaned in places where electronic waste is processed and dumped
Basel Action Network (BAN)

## Slide 32
About to smash CRT to get copper from yoke and releasing a collection of toxic compounds
Basel Action Network (BAN)

## Slide 33
Wires are sorted during the day and burned at night. Burning the PVC and brominated insulation on the wires produces dioxins
Basel Action Network (BAN)

## Slide 34
Girls sorting e-waste components fearful of having picture taken.
Basel Action Network (BAN)

## Slide 35
E-waste that cannot be recycled is discarded along rivers and streams
Basel Action Network (BAN)

## Slide 36
An iMac keyboard produced from 1999 - 2003
Basel Action Network (BAN)

## Slide 37: Accra, Ghana
Notes: pronounced: uh-krAA

## Slide 38: Recycling in Accra, Ghana
Even more primitive and dangerous than Guiyu, China
  Less organized
  Less sorting
E-waste is disassembled in makeshift fashion
Less interest in circuit board components
  Metals are mostly sought after
More burning of e-waste
  creating greater amounts of dioxins

## Slide 39
Worker burns insulation from refrigerator on top of computer
© RENÉE C. BYER

## Slide 40
Power cords, internal wires and a variety of cables are balled up and burned. What’s left in the ashes is melted copper and aluminum
Basel Action Network (BAN)

## Slide 41
The constant burning of e-waste pollutes the ground and air with heavy metals and dioxins
Basel Action Network (BAN)

## Slide 42
Workers are exposed to acute and chronic levels of dioxins
© RENÉE C. BYER

## Slide 43
Individuals scrap through the ashes for bits of metals
Basel Action Network (BAN)

## Slide 44
The once pristine Korle Lagoon is now a toxic dump of e-waste
Basel Action Network (BAN)

## Slide 45
Eight year old child combs through toxic debris attempting to scavenge anything of value
© RENÉE C. BYER

## Slide 46
Ten year old child’s daily existence in the toxic dump of Accra
© RENÉE C. BYER

## Slide 47: Steps to decrease the export of e-waste
US could ratify the Basel Convention
E-recyclers could be regulated and audited
  assuring no e-waste is exported
External costs of e-recycling born by manufacturer
  included in price of component
  incentive for manufacturers to make components profitable to recycle
Increase aid to developing countries

## Slide 48
http://www.state.nj.us/dep/dshw/ewaste/
E-recycling in New Jersey

## Slide 49: Best Buy as a Responsible Solution